## Slide 1: SP-Project
FourYear Transforms

## Slide 2: Part-1

## Slide 3: Problem statement
We are Given Audio Samples of 3 Birds and by Analysis of those that we have to Predict Bird in the Given Test Audios

## Slide 4: FFT of given samples

## Slide 5: Method to distinguish
To distinguish we need to Compare the Nature of FFTs of given samples with the Test Samples and Identify the Bird
So by oberseving the FFTs we can Differentiate them on the basis of Peaks
We normalise the FFT magnitude and Analyse no. of peaks above a certain threshold.

## Slide 6: Method
After Plotting FFT of given Samples, we observe that we can distinguish them based Number of Peaks in Normalised FFT
We choose a Threshold for our Analysis and We can say that if our Test Audio has 0-130 Peaks it is Bird1,if it has 130-400 Peaks it is Bird 2 and if more than this it is Bird 3

## Slide 7: Final Result
Our Code has predicted the Species in Test Samples F1-F8
It can be verified by Observing The FFT plots of those Test Samples

## Slide 8: Part-2

## Slide 9: Problem statement
We are given 3 ECG waves, out of which 2 are noisy
We are tasked to find out the heart rate estimations per minute for each of these ECG waves.

## Slide 10: HR from ECG
In every task we have to find out the heart rate (HR) estimation from ECG wave(s).
From ECG graph we can deduce the heart rate by finding out the RR interval
HR = 60/RR_interval

## Slide 11: ECG_HRConverter
To help with this task, we made a function named ECG_HRConverter.
This function finds R peaks using findpeaks function in matlab and then calculates the heart rate.
This heart rate is averaged out every minute and populates a vector which will be our output

## Slide 12: Task-1
In this task we are required to find out HR for a non noisy ECG E1.
This is a straight forward task, when we employ our custom built function.

## Slide 13: Task-2
Both E2 and E3 signals are noisy. This becomes apparent when we take a look at its FFT.
A low pass filter with cutoff frequency 30hz is enough to filter E2
An additional notch filter for 22hz is employed for E3.

## Slide 16: Part-3

## Slide 17: Problem statement
For Task-1, we are finding the louder words in the given audio samples using the start and end times.
For Task-2, we are finding the louder words in the given audio samples without using the start and end times.

## Slide 18: Task-1
For first subtask I am first finding rms energy of each word using its start time and end time .
Then I am setting a threshold value which filters out the loud words from other words.
Then I have plotted all the words in a histogram where words marked red are having high sounds

## Slide 19: task-1 results

## Slide 20: Task-1 results

## Slide 21: Task-1 results

## Slide 22: Task-1 results

## Slide 23: Task-1 results

## Slide 24: Task-1 results

## Slide 25: Task-1 results

## Slide 26: Task-1 results

## Slide 27: Task-1 results

## Slide 28: Task-2

## Slide 29: Task-2 results

## Slide 30: Task-2 results

## Slide 31: Task-2 results

## Slide 32: Task-2 results

## Slide 33: Task-2 results

## Slide 34: Task-2 results

## Slide 35: Task-2 results

## Slide 36: Task-2 results

## Slide 37: Task-2 results